Panasonic Automotive & Industrial Systems Europe GmbH

Robert-Koch-Strasse 100

85521 Ottobrunn, Germany

eu.industrial.panasonic.com

www.panasonic.eu

Press contact:

Helmut Philipowski

helmut.philipowski@eu.panasonic.com

Phone: +49 89 45354 1427

eu.industrial.panasonic.com

Press enquiries:

Heiko Hespen

Account Director, BWW Communications

Phone: +49 89 42036391

Email: heiko.hespen@bwwcomms.com

New high temperature and high endurance aluminium electrolytic capacitors from Panasonic offer low ESR and high capacitance values

Munich, 7th July 2016: Panasonic Automotive & Industrial Systems Europe is announcing its new V-FT series of aluminium electrolytic capacitors benefiting from a long life time of up to 5000 hours (2.5 times more than current FT series devices) at high temperatures of up to 105°C. Furthermore, the components benefit from high capacitance of up to 2200µF and ESR values that are 40% up to 60% lower than of current FK series products while downsizing by one can size (G to F size).

Additional technical specifications include an operating temperature range of 
-55°C up to + 105°C, a rated voltage range of  6.3V.DC to 50 V.DC, a capacitance tolerance of ±20 % (120 Hz/+20 °C), and a leakage current of ≤ 0.01CV after two minutes. The parts are fully RoHS and AEC-Q200 compliant.

Comments Stefan Fritsch at Panasonic: “Our new V-FT series aluminium electrolytic capacitors are ideal for low ESR applications e.g. ADAS, Body Control Module and LED lighting. They benefit from a long life time that is up to 2.5 times longer than current FT series components while downsizing by one can size compared with current FK series devices.

For further information on the V-FT series aluminium electrolytic capacitors, please visit: https://eu.industrial.panasonic.com/

About PAISEU

Panasonic Automotive and Industrial Systems Europe (PAISEU) is a company that provides unparalleled expertise to leading car manufacturers, industrial customers and OEMs.  It researches, develops, manufactures and supplies key electronic components, devices and modules up to complete solutions across a broad range of industries; and provides production equipment which builds the manufacturing lines of global corporations.

Globally, Panasonic's Automotive and Industrial Systems company is responsible for over one third of Panasonic’s overall revenue.