Panasonic Automotive & Industrial Systems Europe GmbH

Robert-Koch-Strasse 100

85521 Ottobrunn, Germany

eu.industrial.panasonic.com

www.panasonic.eu

Press contact:

Helmut Philipowski

helmut.philipowski@eu.panasonic.com

Phone: +49 89 45354 1427

eu.industrial.panasonic.com

Press enquiries:

Heiko Hespen

Account Director, BWW Communications

Phone: +49 89 42036391

Email: heiko.hespen@bwwcomms.com

Panasonic Releases Improved 2nd Generation of Grid-EYE Infrared Array Sensors

Lower NETD, High accuracy and increased detection distance

Munich, July 2016: Panasonic Automotive & Industrial Systems Europe has released the much improved and accurate second generation of its Grid-EYE infrared array sensors. The new high gain types (AMG8833 and AMG8834) and low gain types (AMG8853 and AMG8854) of Grid-EYE 2nd Generation now benefit from an improved NETD (Noise Equivalent Temperature Difference) of  0.16°C at 10Hz and of 0.05°C at 1 Hz. For all Grid-EYE 2nd Generation models the detection distance has improved from 5m up to 7m. It is important to note that the second generation of Grid-EYE sensors is fully compatible with the existing first generation designs. This means that the engineers can now get improved and accurate results when they use the sensor in their applications. Panasonic is committed to improve the customer experience and provide much more application benefits with the improved MEMS technology.

Based on Panasonic’s MEMS (Micro Electro Mechanical Systems) technology the Grid-EYE 2nd Generation infrared array sensors combine a more sensitive MEMS sensor chip, a digital ASIC (I2C interface) and a silicon lens in the same small package. The parts feature 64 thermopile elements in an 8x8 grid format that detect absolute surface temperature without any contact. Unlike conventional sensors, Grid-EYE uses a patented 60° silicon lens etched out of a silicon wafer, which is (with less than 0.3mm height) the smallest available lens in the market. The combination of these technologies allows for a sensor package size of only 11.6mm x 8mm x 4.3mm, which is around 70% smaller in size than competitor products.

Compared to single element thermopile sensors and pyroelectric sensors, the  Grid-EYE 2nd Generation can not only detect moving and motionless people and objects but does that in comparison to its predecessor models with higher precision and higher  accuracy.

For more information on the new Grid-EYE 2nd Generation sensors from Panasonic please visit: https://eu.industrial.panasonic.com/products/sensors-optical-devices/sensors-automotive-and-industrial-applications/infrared-array

About PAISEU

Panasonic Automotive & Industrial Systems Europe (PAISEU) is a company that provides unparalleled expertise to leading car manufacturers, industrial customers and OEMs.  It researches, develops, manufactures and supplies key electronic components, devices and modules up to complete solutions across a broad range of industries; and provides production equipment which builds the manufacturing lines of global corporations. Globally, Panasonic's Automotive & Industrial Systems is responsible for over one third of Panasonic’s overall revenue.

For further product information, please visit: http://eu.industrial.panasonic.com/